## Slide 1: GP14 Cruiser Training Course
Shore Session/s
Communications & Distress Signals
Copyright Oliver L. Shaw, 2019

## Slide 2: Distress Signals
Three broad types
  Electronic Distress Signals
  Pyrotechnic Flares
  Others
    Last resort, for when nothing else is available, e.g.
      Flames on vessel (!!)
      Morse SOS, by any method
      Slowly raising and lowering arms
      Continuous sounding of any gun or fog signal apparatus
      Etc.

## Slide 3: Distress Signals
Electronic Distress Signals
  The standard recommendation nowadays

## Slide 4: Distress Signals
Pyrotechnic Flares
  Old and well proven technology
  Distress only (plus white for collision avoidance)
Limitations / Problems
  May or may not be seen
  May or may not be recognised even if seen
  Very limited burn time
  Potentially very dangerous
  Only 3 year shelf life, then very expensive to replace
  Major problems of disposal at end of life

## Slide 5: Distress Signals
Pyrotechnic Flares - Problems
  May or may not be seen
    Short burn time
    Pure chance whether anyone happens to be looking in the right direction
    … and visibility may be impaired by weather - including low cloud
  May or may not be recognised even if seen
    Especially if only person to see it is a lay person
  Very limited burn time
    1 to 3 minutes, depending on type of flare
  Potentially very dangerous
    Especially if flare malfunctions
      Has happened even when well within date
    Fire / explosion / burns / shooting oneself; all possible - and all have happened!
      Even with professionally trained and expert users!
  Only 3 year shelf life, then very expensive to replace
  Major problems of disposal at end of life

## Slide 6: Distress Signals
Pyrotechnic Flares
  Problems
    Distress only (plus white for collision avoidance)
    May or may not be seen
    May or may not be recognised even if seen
    Very limited burn time
    Potentially very dangerous
    Only 3 year shelf life, then very expensive to replace
    Major problems of disposal at end of life
Electronic alternatives have many advantages!

## Slide 7: Distress Signals
Electronic alternatives have many advantages!
  Potential for two-way communication
    So you then know when call has been received
    And can discuss / liaise with Coastguard, etc.
  Relatively long transmitting time
    EPIRB at least 48 hours; PLB at least 24 hours
    Handheld VHF radio typically several hours of two-way communication
    Not just a couple of minutes
  No safety hazard
    (fire, explosion, burns, shooting oneself, etc)
  Indefinite lifetime
    No need to replace every three years
    Just need periodic replacement of batteries
  No end of life disposal problems

## Slide 8: Communications, & Distress Signals
By far the best 2-way short range communications system is a hand-held marine VHF.
  Can be used for distress communications, but also for much else.
  Ideally worn on the person; if you go MOB, a radio still in the boat may not be much help!
  Entry level sets are currently around £60 (e.g. the cheapest of the Cobra range)
  Market leaders are probably Icom (the professionals’ choice) and Standard Horizon (cheaper than Icom, but still very good).
  At the top end, modern sets offer a vast array of additional features, at a price.
  You personally will need an Operating Licence, for which you will need the appropriate certificate.
  Many sailing clubs offer courses for this qualification, or the RYA do an online course - but you still then need to do the examination.
  You also need a separate licence for the set itself (Ship Portable Radio Licence); free if you apply online.

## Slide 9: Communications, & Distress Signals
By far the best 2-way short range communications system is a hand-held marine VHF.
Can be used for distress communications, but also for much else.
  Port Control: Information on shipping movements
  Port Control and Coastguard: Navigational warnings
  Port Control and Coastguard: Weather forecasts
  Liaison with Coastguard / harbours / (marinas)
  Liaison with sailing club / escort boats / other dinghies in fleet
  Etc., etc.
  The standard means of short-range communication (up to a few miles between dinghies, up to 25 miles between boat and Coastguard)

## Slide 10: Communications, & Distress Signals
By far the best (one-way) long-distance distress alert system is a Personal Locator Beacon (PLB) or an Electronic Position Indicating Radio Beacon (EPIRB).
  PLBs are specifically designed to be worn on the person. EPIRBS are designed to be carried aboard the boat.
  This is one-way only. Once activated it broadcasts a continual distress signal for at least 24 hours (for a PLB, 48 hours for an EPIRB) to a satellite, which is then forwarded to the appropriate rescue co-ordination centre.
  It can take much longer to alert the authorities than calling the Coastguard direct on VHF, up to 2 hours (because it may have to wait for a satellite), but there is a guarantee that the signal will get through and that a rescue will be triggered.
  An excellent back-up if you are out of range of VHF (unlikely in a dinghy), or in a VHF black-spot (which is entirely possible)

## Slide 11: Communications, & Distress Signals
VHF | PLB / EPIRB
Two way | One way
Short range (Up to about 25 miles) | Long distance (World wide)
All communications | Distress only
Will probably be picked up | Will definitely be picked up
Immediate response, provided it is picked up at all | Can take up to 2 hours to raise the alert
Alerts all vessels within range | Alerts rescue authority only
Immediate, but not guaranteed
Guaranteed, but not immediate

## Slide 12: Communications, & Distress Signals
The RYA SAFE-TRX system
  A smartphone app which monitors your boat journeys and alerts designated emergency contacts should you fail to arrive on time.
  Runs your phone’s GPS continuously, so potentially very heavy battery drain …
  … so you may need a backup power source or a means of recharging battery onboard
  Designed for small boat users, and particularly for those who don’t carry VHF and PLB/EPIRB
  Of limited use (perhaps no use) in areas of poor phone signal.
    Potential for false alerts if you had signal when you set off but none on arrival.
  Phone needs to be in waterproof case at all times
  Free to download, and free to use.
  https://www.rya.org.uk/knowledge-advice/safe-boating/keep-in-touch/Pages/safetrx.aspx
NB. Second-best

## Slide 13: Communications, & Distress Signals
Very much the poor relation; a mobile phone
  Absolutely must either be a waterproof model (which is a very rare beast, although they do exist) or be kept at all times in a waterproof case - even when in use.
  Mobile phones drown very rapidly when immersed !!!
  Conversations are intrinsically private - so other boat owners in your immediate area who may be in a position to assist don’t get to know that you are in trouble.
  Signal coverage of coastal areas has improved in recent years, but it is still patchy.

## Slide 14: Communications, & Distress Signals
The “Final Mile”
  When rescue asset is in sight, to enable them to find you.
  By Day:
    Liaise by radio, give them a bearing (if you have a compass), and make a visual signal -
      Orange smoke flare
      Hand-held red flare
      High intensity LED safety “flare”, such as ODEO, or (very much perhaps) cheaper non-marine alternatives
      Wave oar or paddle in the air (you will normally have one or other available).

## Slide 15: Communications, & Distress Signals
The “Final Mile”
  When rescue asset is in sight, to enable them to find you.
  By Night:
    Liaise by radio, give them a bearing (if you have a compass), and make a visual signal -
      Hand-held red flare
      High intensity LED safety “flare”, such as ODEO, or (very much perhaps) cheaper non-marine alternatives
      Powerful torch

## Slide 16: Communications, & Distress Signals
The “Final Mile”
  When rescue asset is in sight, to enable them to find you.
  If you are MOB and separated from boat:
    Liaise by radio; an excellent reason for wearing it on your person!
    Wave an arm as near vertical as possible
    Light on your buoyancy device
    Personal day/night flare, carried permanently on your person.

## Slide 17
** Copyright **
Copyright Oliver L. Shaw, 2019
  All enquiries, including requests for permission to copy, to
  the author, Oliver L. Shaw, at any of the following addresses:
    71 Brodie Avenue, Mossley Hill, Liverpool, L18 4RE
    c/o Liverpool Sailing Club
    c/o Mr T J Vogel, The Chamber of Experts, 48 The Street, Sporle, Swaffham, PE32 2DR.